## Slide 1
L.R. Baylor, S.J. Meitner,
S.K. Combs, G.E. Gebhart,
D. Rasmussen*, M. Lyttle*, P.B. Parks#
ORNL, *USITER, #GA
M. Lehnen, S. Maruyama, U. Kruezi
ITER
J. Wilson, G. Ellwood, A. Muir
JET- CCFE
Theory and Simulation of Disruptions Workshop, PPPL
17-July-2017
Developments in Shattered Pellet Technology and Implementation on JET and ITER

## Slide 2: Outline
SPI R&D overview
SPI Deployment on JET
ITER DMS Issues for SPI
JET SPI experimental opportunities
  U.S. input to the JET disruption taskforce: proposal titles due Aug. 4, full proposals in Sept.

## Slide 3: SPI: History
D2 fueling pellets hitting an inclined plate shatter when the normal velocity >30 m/s.
This motivated the development of shatter plates and tubes to form collimated sprays of pellet material that penetrate deeply in a short duration.
The shattered material prevents impact damage to the first wall and increases ablation.
Mixed species D2/Ne SPI allows control of mitigated disruption properties
Pellets are known to shatter when hitting a surface with enough perpendicular velocity
Combs, et al.

## Slide 4: Shattering Occurs from Transit Through Bent Tube Resulting in ~15o Dispersion
Foil
Impacts
Neon Pellet in 20o Shatter Tube

## Slide 5
Shattered Pellet Injection (SPI) shows benefits over Massive Gas Injection (MGI) – only used on DIII-D
SPI
MGI
#128227
“normal” view using the fast framing camera
Thermal Quench
Current Quench
TQ
CQ
#138212
#138212
Commaux, et al., Nucl. Fus. 2011
Fast visible camera images

## Slide 6: 3-Barrel SPI design has been developed for ITER and deployed on DIII-D and soon on JET
Barrel inner diameter can vary in order to study scaling of D2 and neon SPI
SPI uses MGI like valves to accelerate pellets and can be used as MGI system when no pellet is formed.
D2, D2/Ne, Ne, Ar* are possible
View of freezing process from end of barrel

## Slide 7
Experimental Density (g/cm3)
Predicted Density (g/cm3)
Alloy Model
Average Model
Mixed D2/Neon Pellet Density Agrees
with the Alloy-Based Model
The required SPI pellet size for a given mixture ratio and quantity of material is now well understood. (Parks 2017)

## Slide 8
Mass (g)
Speed (m/s)
Mixed D2/Neon Pellet Speed Decreases as the Neon Fraction and Pellet Mass Increases
The SPI pellet speed is a strong function of the mass for a given pellet size and gas valve pressure as expected from ideal gun theory. A factor of 2 range in speed is expected for SPI D2/Ne mixtures.

## Slide 9: Argon SPI pellets have now been made and shot with the use of a gas driven mechanical punch
The argon triple point of 87K is much higher than that of Ne (24.5K) and D2 (18.7K). Mixtures with Ar are there not possible. Layered pellets with Ar in front or rear are possible.
Cold Zone
Argon and pure neon (with no D2 shell) are difficult to break free from the cold barrel with gas. A mechanical punch is employed to break the pellet free, then gas accelerates it.
Combs, 2015
Fast Camera
Ar
D2

## Slide 10: A typical Argon SPI post-shatter particle size distribution determined from the fast camera data
Argon formed at 30 K
650 mbar L of Ar
L/D = 1.51
Fired at 55 K
Speed = 156 m/s
Mass of Pellet = 1.18 g
Mass of Particles = 1.14 g
Chart: Rough Particle Size Distribution for Shot 10122
| Less Than 1 | 1 to 2 | 2 to 3 | 3 to 4 | Greater Than 4
 | 77 | 35 | 23 | 11 | 5
V = 156 m/s
T. Gebhart, 2017

## Slide 11
The particle size distribution compares favorably to a Statistical Fragmentation Model by Parks
based on Energy and Maximal Entropy
Ar SPI

## Slide 12
The particle size distribution for D2 pellets also compares favorably to the Statistical Fragmentation Model
16mm D2 Test, Commaux 2009
D2 SPI

## Slide 13
Pressure in the valve can be used to determine whether or not the pellet was successfully fired
Explanation of Shots:
Shot 8640 (Green) – Pellet stuck and gas penetrated through center.
Shot 8642 (Blue) – Valve shot with no pellet or mass in barrel.
Shot 8644 (Red) – Pellet stuck and pressure slowly released.
Shot 8647 (Black) – Pellet fired after sticking in the barrel for 25 ms.
Shot 8649 (Yellow) – Good shot, 50-50 D2-Ne mix, 405 m/s.
System Parameters:
16.5 mm Barrel ID (16.5mm diameter pellets)
Large Orifice Valve Operated at 600 PSI , 0.85 L
1 Volt = ~13.8 Bar (200 PSI)

## Slide 14: Outline
SPI R&D overview
SPI Deployment on JET
ITER DMS Issues for SPI
JET SPI experimental opportunities
  U.S. input to the JET disruption taskforce: proposal titles due Aug. 4, full proposals in Sept.

## Slide 15
JET provides extrapolation toward ITER and future fusion system energy dissipation needs
1022
1023
1025
1024
Pellet Atoms (Neon)

## Slide 16: SPI 3-barrel concept for ITER to be deployed on DIII-D and JET to help answer key questions for ITER
SPI2 has been installed and on DIII-D in February 2017– initial experiments under way. (D. Shiraki, N, Eidietis)
3 pellets can be fired together or serially.
An SPI for JET has been designed based on the same design. Limits
pellet size to 12.5mm (6 bar-L of neon).
Major difference is Tritium compatibility requiring more rigorous QA. Good practice for ITER.

## Slide 17: JET SPI capabilities
Three pellets of different sizes
    D2/Ne/Ar or D2/Ne mixture
    ~0.1 bar.L to 6 bar.L (1021 – 1023) per pellet
    12.5*, 8, 4 mm sizes - *argon punch
Independent firing
    timed or simultaneous (±0.2ms)
    (signal delay TBC)
Pellet speed ~100–250m/s (max 500m/s with D2)
    flight time ~20-50ms
    Plasma edge arrival time known to <2 ms
Notes: Layered pellets possible (D2 jacket, front/back doping)
No. of atoms roughly similar for all three gases for the same barrel. Middle barrel payload is approximately the geometric mean of the largest and smallest.

## Slide 18: SPI Configuration on JET
JET SPI to be located where DMV1 was installed for vertical injection
The 40mm opening constrains the shatter tube geometry that can be employed.

## Slide 19: JET SPI capabilities
Microwave cavity diagnostic
    Pellet mass* (amplitude ~ mass)
    Velocity ± 10% (perturbation width)
    Pellet integrity (early/late peaks)
*Pellet mass determined by reservoir ΔP during formation
J. Caughman, 2017

## Slide 20: JET SPI capabilities
Shatter cone facing High Field Side
    20 degree bend in injection tube pointed to HFS
    Intercept/disperse REs created by DMV3
Tube geometry: good collimation
    Fragments too small to damage PFCs
    Large enough for good penetration

## Slide 21: The JET shatter tube was tested at ORNL using argon pellets launched with a prototype mechanical punch
Cut away model of the JET shatter tube
JET shatter tube installed on test stand in Pellet Lab
Exit of shatter tube as viewed by the fast camera
Punch Face
Connection to Propellant Valve
Pellet
Punch Schematics
S. Meitner,

## Slide 22: JET SPI capabilities
Pellets of <15 m/s survived the shatter tube intact
    12.5mm argon pellet of 6g has only 1 J of kinetic energy – no danger to JET inner wall
Largest pellet could have up to 180J of kinetic energy, must be interlocked to prevent hitting the closed TIV

## Slide 23: Outline
SPI R&D overview
SPI Deployment on JET
ITER DMS Issues for SPI
JET SPI experimental opportunities
  U.S. input to the JET disruption taskforce: proposal titles due Aug. 4, full proposals in Sept.

## Slide 24: ITER SPI Configuration
Pellet sizes chosen based on IO requirements, available space, and lab results
Pellet | OD (mm) | L/D | Qty | Location
Size 1 | 13.39 | 1.5 | 3 | One each UPP 2, 8, 14
Size 2 | 16.56 | 1.5 | 4 | One each UPP 2, 8, 14 EPP 08
Size 3 | 19.74 | 1.5 | 4 | One each UPP 2, 8, 14 EPP 08
Size 4 | 28.45 | 2.0 | 14 | All in EPP08
Injectable amounts for Ne shell pellet
TLM: up to 9.6 kPa*m3
RES: up to 76.6 kPa*m3
Requires ~90 kPa*m3 of He propellant gas required to maximize speed (challenges vacuum system)

## Slide 25: Design Issue #1 - Upper Port Exit Angle
20o
Upper ports do not aim towards center of plasma
SPI requires 20 degrees or less for proper shattering
This angle only hits the top of the plasma
Experiment is planned on DIII-D to determine if UPP SPI geometry is viable

## Slide 26
Iso View
Not shown: transport through port plug
Design Issue #2 – No space for Microwave Cavity
MW Cavity Out of Port
MW Cavity In Port
MW Cavity causes clashes
MW Cavity not included in the baseline design
Other diagnostics are needed (e.g. pressure trace, Vis-IR plasma view)
Shielding compromised
Clash w/ Bioshield

## Slide 27: Design Issue #3 – Upper Port Path
Funnel (2o)
Valve
Bends (2o)
Bellows/Funnel
Funnel (2o)
Coupling/funnel
Bends (2.5o)
Pellet speed and/or pellet survivability are likely to be limited by this configuration
Previous testing at ORNL shows bends over 2o are likely to break pellets
New tests underway to expand on previous testing and to verify ITER geometry

## Slide 28: Outline
SPI R&D overview
SPI Deployment on JET
ITER DMS Issues for SPI
JET SPI experimental opportunities
  U.S. input to the JET disruption taskforce: proposal titles due Aug. 4, full proposals in Sept.

## Slide 29: JET SPI Experimental opportunities
RE Studies
RE dissipation with Ar/Ne SPI using punch
  Working on variation of particle size as function of speed – possible knob
  Multiple pellets possible – Ar, Ne
  JET is working on vertical position control to allow results
RE Avoidance – D2/Ne mixtures, possible Ar-D2 layer pellets
  High current operation?

## Slide 30
Thermal Mitigation – Small pellet sizes
Optimization of D2/Ne mixture
  May need punch for small pellet size to vary pellet speed
TM with fixed amount of Ne and different amounts of D2 (vary pellet size)
Mitigation of a near disrupting plasma – wounded duck
  Dependence on locked mode location WRT SPI location
JET SPI Experimental opportunities

## Slide 31: Summary
SPI R&D is ongoing to quantify shattering and capabilities for ITER configurations.
The need for a reliable DMS on ITER have motivated a strong international effort on JET (ITER, USITER, USDOE, EUROfusion, CCFE all working well together)
SPI will be installed on JET in Sept. for experiments starting in 2018, and could be integrated into JET DMS in future.
JET SPI Benefits to ITER
  Commissioning and Operational Experience
  Data on TM heat loads, halo currents, and RE mitigation
  Modeling, simulation, extrapolation to ITER
U.S. input to the JET disruption taskforce: proposal titles due Aug. 4, full proposals in Sept.